RF Quadrature (IQ) Signals
Math Model
Hardware Implementation
Digital Data Representation
Software Implementation
Spiro Sarris. 12 / 2018
A cdot cos( %omega cdot t + %phi )

---
Outline
1. Amplitude, phase. Why is it interesting?
2. Euler’s formula
3. Mathematical model of signal
4. Implementation of model in receiver hardware
5. Analog to digital conversion (ADC)
6. Convenience in software programming languages
7. Implementation of model in software
8. Tradeoffs between I/Q sampling and real-value sampling
9. Python demonstration

---
1. Amplitude, Phase
Amplitude, A
time
Phase, Φ
ΔΦ = 2π
ΔΦ = 2π radians for 1 cycle in time and for 1 wavelength (λ) [m] in space
Angular frequency (ω) [radians/sec] is the rate of change of phase vs. time
Temporal frequency (f) [Hz] is the number of cycles per second
%omega = {d%phi} over {dt}
f = %omega over { 2%pi }

---
1. Amplitude
RSSI – Received Signal Strength Indicator
Communication Modulation
Component Gain / Loss
Synthetic Aperture Radar Image

---
1. Phase
Data Communication Modulation
Length / Distance Measurement
Synthetic Aperture Radar Interferometer
Radio Interferometer

---
2. Euler’s Formula
j=sqrt{ -1 }
A cdot e^{j cdot %phi} = A cdot [ cos( %phi )+j cdot sin( %phi )]
- Year 1748 - Mathematician Leonhard Euler published that periodic functions such as cosine and sine can be represented as complex exponentials of instantaneous phase (phasors)
- This model simplifies math related to amplitude and phase

---
3. Mathematical Model of Signal
Antenna
Balun
V(t) = A cdot cos(2 %pi ft + %phi)
S[n ] = A cdot cos( 2 %pi nT_{s} + %phi )
n is integer index for discrete time
t in continuous time
At any location in space, we can measure real-valued voltage and record with ADC. Recorded data includes only instantaneous amplitude. How do we find the phase information?

---
3. Mathematical Model of Signal
Euler’s model of complex phasor
Real-value cosine
?
Receiver
V(t) = A cdot cos(2 %pi ft + %phi)
A cdot e^{j cdot %phi} = A cdot [ cos( %phi )+j cdot sin( %phi )]
How can we translate real-value voltage signal model (easy to understand in the physical world) to quadrature I/Q signal model (easy to process using DSP software)?

---
4.Implementation of Model in Hardware
I/Q Downconverter Receiver (example from Ettus USRP N210 + WBX)

---
4. I/Q Downconverter Receiver
V_{1}( t ) = A cdot cos(%phi(t)) = A cdot cos( 2 %pi f _{RF}t+%phi_0)
4
2
Use trig identity – product to sum
1
V_{2}( t ) = A cdot cos( 2 %pi f_{RF}t+%phi_{0}) cdot cos( 2 %pi f_{LO}t+%phi_{LO} ) ...
A cdot cos[ 2 %pi (f_{RF}+f_{LO})t + %phi]+A cdot cos[ 2 %pi (f_{RF}-f_{LO})t + %phi]
Lowpass filter removes
V_{3}( t ) = A cdot cos( 2 %pi f_{RF}t+%phi_{0}) cdot cos( 2 %pi f_{LO}t+%phi_{LO} -{%pi} over {2} ) ...
90 degree
phase delay
A cdot cos( 2 %pi f_{RF}t+%phi) cdot sin( 2 %pi f_{LO}t) ...
A cdot cos[ 2 %pi (f_{RF}+f_{LO})t + %phi ]+A cdot sin[ 2 %pi (f_{RF}-f_{LO})t + %phi]
5
3
Lowpass filter removes
f_{ IF }=f_{RF}-f_{LO}
V_{4}( t ) = A cdot cos[ 2 %pi (f_{RF}-f_{LO})t + %phi]
V_{4}( t ) = A cdot cos[ 2 %pi f_{IF}t + %phi ]
V_{5}( t ) = A cdot sin[ 2 %pi (f_{RF}-f_{LO})t + %phi ]
V_{5}( t ) = A cdot sin[ 2 %pi f_{IF}t + %phi]

---
5. Analog to Digital Conversion
2 ADCs with same sample clock and same length of cable / PCB trace
4
Assume 8-bit ADC
Channel I “in phase”
S_{I}[n ] = A cdot cos( 2 %pi f_{IF}nT_{s} + %phi )
S_{Q}[n ] = A cdot sin(2 %pi f_{IF}nT_{s} + %phi )
Channel Q “quadrature phase”
(delay by π/2 radians = λ / 4)
How to combine … ?
5
NOTE: ‘I’ and ‘Q’ in this context are for 1 polarization. Not related to Stokes parameters {I, Q, U, V}
S_{IQ}[n ] = S_{ I }[ n ]+j cdot S_{ Q }[ n ] = A cdot e^{j(2 %pi f_{IF}nT_s+ %phi)}

---
5. Analog to Digital Conversion

---
6. Convenience in Software
- Programming languages include support for complex/imaginary numbers and exponential function.
- Many libraries of software are available to process data in this format
Language
Python	1j	numpy.exp(x)
Matlab	J, j, I, i	exp(x)
C	<complex.h> I	<complex.h> cexp(x)
Octave	J, j, I, i	exp(x)
function e^x
symbol sqrt-1

---
6. Convenience in Software
- import numpy as np
- import matplotlib
- matplotlib.use("QT4Agg")
- import matplotlib.pyplot as plt
- fftsize = 1024
- nsamples = 1024
- fs = 8e6
- tt = np.arange(0,nsamples)/fs
- ff = np.linspace(-fs/2,fs/2,fftsize)
- ftest = 100
- fp = open('/home/ssarris/demo.iq','rb')
- fp.seek(0,0)
- dt = np.dtype([('i',np.float32),('q',np.float32)])
- data = np.fromfile(fp,dtype=dt,count=nsamples)
- sigt = data['i']+1j*data['q']
- sigf = np.fft.fft(sigt,fftsize)
S_{IQ}[n ] = S_{ I }[ n ]+j cdot S_{ Q }[ n ] = e^{( j2 %pi f_{IF}nT_s+ %phi )}

---
7. Software Implementation
- Single-phase downconverter (not I/Q)
- Same math from page 10-11 but remove hardware and data of Q channel
Assume 8-bit ADC
4
2
Channel I “in phase”
byte 0	byte 1	byte 2	byte n
I[0]	I[1]	I[2]	I[n]
1
X
X
X
X
V_{4}( t ) = A cdot cos[ 2 %pi f_{IF}t + %phi ]
S_{I}[n ] = A cdot cos( 2 %pi f_{IF}nT_{s} + %phi )
How to create the ‘Q’ component … ?
S_{IQ}[n ] = S_{ I }[ n ]+j cdot S_{ Q }[ n ] = A cdot e^{j(2 %pi f_{IF}nT_s+ %phi)}

---
7. Hilbert Transform
Create the complex-valued analytic signal by Hilbert transform of the real-valued signal
S_{IQ}[n] = HILBERT ( S_I[n] ) = IFFT( FFT(S_{I}[n]) cdot 2 cdot UNITSTEP[n] )
Function is available in Python : scipy.signal.hilbert()
Convenient, but output of Hilbert() bytes of data is 2x input bytes
Insert code snippet
Insert graph

---
8. Tradeoff: Real-value vs I/Q sampling
- TODO – graphic of spectrum.
- TODO – graphic of streams of bytes. Overall samples and total data rate is the same.