RF Quadrature Signals
Mathematical Model
Hardware Implementation of Model
Digital Data Representation
Spiro Sarris. 07 / 2018
A cdot cos( %omega cdot t + %phi )

---
Outline
1. Amplitude, phase. Why is it interesting?
2. Euler’s formula
3. Mathematical model of signal
4. Receiver hardware implementation of model
5. Analog to digital conversion
6. Convenience in software
7. Tradeoffs between I/Q sampling and real-value sampling

---
1. Amplitude, Phase
Amplitude, A
time
Phase, Φ
ΔΦ = 2π
ΔΦ = 2π radians for 1 cycle in time and for 1 wavelength (λ) [m] in space
Angular frequency (ω) [radians/sec] is the rate of change of phase vs. time
Temporal frequency (f) [Hz] is the number of cycles per second
%omega = {d%phi} over {dt}
f = %omega over { 2%pi }

---
1. Amplitude
RSSI – Received Signal Strength Indicator
Communication Modulation
Component Gain / Loss
Synthetic Aperture Radar Image

---
1. Phase
Data Communication Modulation
Length / Distance Measurement
Synthetic Aperture Radar Interferometer
Radio Interferometer

---
2. Euler’s Formula
j=sqrt{ -1 }
A cdot e^{j cdot %phi} = A cdot [ cos( %phi )+j cdot sin( %phi )]
- Year 1748 - Mathematician Leonhard Euler published that periodic functions such as cosine and sine can be represented as complex exponentials of instantaneous phase (phasors)
- This model simplifies math related to amplitude and phase

---
3. Mathematical Model of Signal
Antenna
Balun
V(t) = A cdot cos(2 %pi ft + %phi)
S[n ] = A cdot cos( 2 %pi nT_{s} + %phi )
n is integer index for discrete time
t in continuous time
At any point in space, we can measure real-valued cosine. Convenient, but .. not ideal for DSP software that requires quadrature sampled signal.

---
3. Mathematical Model of Signal
Euler’s model of complex phasor
Real-value cosine
?
Receiver
V(t) = A cdot cos(2 %pi ft + %phi)
A cdot e^{j cdot %phi} = A cdot [ cos( %phi )+j cdot sin( %phi )]
How can we translate real-value signal model (easy to understand in the physical world) to quadrature I/Q signal model (easy to process using DSP software)?

---
4. Hardware Implementation of Model
Option 1- Direct Conversion Receiver (example from Ettus USRP N210 + WBX)

---
4. Direct Conversion Receiver
V_{1}( t ) = A cdot cos( 2 %pi f _{RF}t+%phi_{0})
4
Use trig identity – product to sum
2
V_{2}( t ) = A cdot cos( 2 %pi f_{RF}t+%phi_{0}) cdot cos( 2 %pi f_{LO}t ) ...
1
A cdot cos[ 2 %pi (f_{RF}+f_{LO})t + %phi]+A cdot cos[ 2 %pi (f_{RF}-f_{LO})t + %phi]
Lowpass filter removes
V_{3}( t ) = A cdot cos( 2 %pi f_{RF}t+%phi_{0}) cdot cos( 2 %pi f_{LO}t -{%pi} over {2} ) ...
90 degree
phase shift
A cdot cos( 2 %pi f_{RF}t+%phi) cdot sin( 2 %pi f_{LO}t) ...
A cdot cos[ 2 %pi (f_{RF}+f_{LO})t + %phi ]+A cdot sin[ 2 %pi (f_{RF}-f_{LO})t + %phi]
5
3
Lowpass filter removes
V_{4}( t ) = A cdot cos[ 2 %pi (f_{RF}-f_{LO})t + %phi]
f_{ IF }=f_{RF}-f_{LO}
V_{5}( t ) = A cdot sin[ 2 %pi (f_{RF}-f_{LO})t + %phi ]
V_{4}( t ) = A cdot cos[ 2 %pi f_{IF}t + %phi ]
V_{5}( t ) = A cdot sin[ 2 %pi f_{IF}t + %phi]

---
5. Analog to Digital Conversion
2 ADCs with same sample clock and same length of cable / PCB trace
4
Channel I
byte 0	byte 2	byte 4	byte 2*n
I[0]	I[1]	I[2]	I[n]
S_{I}[n ] = A cdot cos( 2 %pi f_{IF}nT_{s} + %phi )
byte 0	byte 2	byte 4	byte 2*n
Q[0]	Q[1]	Q[2]	Q[n]
S_{Q}[n ] = A cdot sin(2 %pi f_{IF}nT_{s} + %phi )
Channel Q
Translate?
5
How to combine I and Q channel data into complex exponential (phasor) in software?
S_{iq}[n ] = S_{ I }[ n ]+j cdot S_{ Q }[ n ] = e^{j(2 %pi f_{IF}nT_s+ %phi)}

---
6. Convenience in Software
- Programming languages include support for complex/imaginary numbers and exponential function.
- Many libraries of software are available to process data in this format
Language
Python	1j	numpy.exp(x)
Matlab	J, j, I, i	exp(x)
C	<complex.h> I	<complex.h> cexp(x)
Octave	J, j, I, i	exp(x)
e^x
sqrt-1

---
6. Convenience in Software
- import numpy as np
- import matplotlib
- matplotlib.use("QT4Agg")
- import matplotlib.pyplot as plt
- fftsize = 1024
- nsamples = 1024
- fs = 8e6
- tt = np.arange(0,nsamples)/fs
- ff = np.linspace(-fs/2,fs/2,fftsize)
- ftest = 100
- fp = open('/home/ssarris/demo.iq','rb')
- fp.seek(0,0)
- dt = np.dtype([('i',np.float32),('q',np.float32)])
- data = np.fromfile(fp,dtype=dt,count=nsamples)
- sigt = data['i']+1j*data['q']
- sigf = np.fft.fft(sigt,fftsize)
S_{iq}[n ] = S_{ I }[ n ]+j cdot S_{ Q }[ n ] = e^{( j2 %pi f_{IF}nT_s+ %phi )}

---
7. Tradeoff: Real-value vs I/Q sampling
- TODO – graphic of spectrum.
- TODO – graphic of streams of bytes. Overall samples and total data rate is the same.